| Direction Cosines of Vectors Perpendicular to Planes: |
| --- |
| Plane: | x | y | z |
| Cross-section of Common Rafter = Purlin Face Perpendicular to Roof Plane | 0 | cos SS | sin SS |
| Side Face of Common Rafter | 1 | 0 | 0 |
| Roof Plane = Backing Plane | 0 | sin SS | - cos SS |
| Cross- Section of Hip / Valley | cos DD cos R1 | sin DD cos R1 | sin R1 |
| Side Face of Hip / Valley | sin DD | - cos DD | 0 |
| Bottom Face of Hip / Valley | cos DD sin R1 | sin DD sin R1 | - cos R1 |
| Deck Plane | 0 | 0 | 1 |
| Plumb Plane thru Eave or Ridge | 0 | 1 | 0 |
| Square Cut on Jack Rafter | cos DD | sin DD | 0 |
| Square Cut on Jack Purlin | cos DD cos (R1 + R2) | sin DD cos (R1 + R2) | sin (R1 + R2) |

To evaluate the dihedral angle, between two planes, substitute values from the table in the equation:

arcos±(x1x2 + y1y2 + z1z2)

Required blade angle setting, :

If  90,  = 90  if  90, 