An ALTERNATE MODEL for HIP / VALLEY RAFTERS:

An ALTERNATE MODEL for HIP / VALLEY RAFTERS:

Kernels of R4, R5 and A5 Angles

GENERAL HIP / VALLEY MODEL:

VALLEY meets RIDGE or HEADER

VALLEY meets MAIN COMMON RAFTER

VALLEY meets MAIN PURLIN

GENERAL HIP / VALLEY MODEL:

Kernels extracted from the general model

GENERAL HIP / VALLEY MODEL:

Kernels rotated and re-scaled

VALLEY ANGLE FORMULAS:

| Valley Peak meets Main Purlin | KNOWN EQUATION | Valley Foot meets Main Common Rafter |
| --- | --- | --- |
| tanR2 = tanC5 tanR3 tanR3 = tanR2 / tanC5 | (From “Extracting the Purlin kernel from the Hip kernel”) tanP1 = tanSS tanP2 | tanR1 = tanC5 tan(90-R4P) tanR4P = tanC5 / tanR1 |
| Divide the kernel along dihedral angle 90–C2, producing two standard Hip kernels. Consider the kernel on the left hand side: | Divide the kernel along dihedral angle 90–A5P, producing two standard Hip kernels. Consider the kernel on the left hand side: |
| cosC1 = sinC2 / sinR2 sinC2 = sinR2 cos C1 | cosC1 = sinC5 / sinP1 | cosDD = sinA5P / sinR1 sinA5P = sinR1 cos DD |
| cos(90- Q2) = cosR3 / cosC1 sinQ2 = cosR3 / cosC1 | cosR2 = cosP2 / cosC1 | cosR5P = cos(90-R4P) / cosDD cosR5P =sin R4P / cosDD |
| tan(90-R2) = tan(90-C2)sin(90-R3) tanC2 = tanR2 cosR3 | (From Standard Hip kernel) tanR1 = tanSS sinDD | tan(90-R1) = tan(90-A5P) sinR4P tanA5P = tanR1 sinR4P |
| Consider the standard Hip kernels created on the right hand side: |
| tan(90-C5) = tan(90-C2) sinR3 tanC2 = tanC5 sinR3 | tanR1 = tanSS sinDD | tan(90-C5) = tan(90-A5P) sin(90-R4P) tanA5P = tanC5 cosR4P |
| tan(90-P2) = sin(90-C5) / tanR3 tanR3 = tanP2 cosC5 | tanC5 = sinR1 / tanDD | tanP2 = sin(90-C5) / tan(90-R4P) tanR4P = tanP2 / cosC5 |
| The process may be continued, using any known formula as a template (for example, tanP2 = cosSS / tanDD), and substituting cognate angles from the unsolved kernel. Remember to compensate for trig functions of complementary angles. The next diagram depicts an alternate method of extracting Hip kernels from the general model. Rotate any appropriate face to the deck, and apply the methods outlined above to obtain solutions. |

GENERAL HIP / VALLEY MODEL:

Standard kernels extracted from General Model

(kernels re-scaled for clarity)

EXTRACTING KERNELS from “the STICK”:

EXTRACTING KERNELS from “the STICK”:

# Text boxes

# D

# 90 – DD

# DD

# DD

### Plan

##### R4Bm

##### R4Pa

##### R4Pm

#### R4Ba

##### P6m

##### SS

##### R5Pm

##### R1

##### R5Bm

##### Dihedral angle = 90 – A5Ba

##### Dihedral angle = 90 – A5Pa

# D

# DD

##### Dihedral angle = 90 – A5Bm

##### Dihedral angle = 90 – A5Pm

##### SS

### cos2 DD tan R1

### tan R1

### 1 / sin DD

### cos DD

The triangle showing angles labeled Q2 and P1 defines the plane of the Main Purlin  perpendicular to the Roof plane.

Other angular values to expect at the intercept of the Purlin plane and the bottom face of the Hip/Valley: R3, P3, C2, C1, R2

### Hip run = 1

## Isometric

Projection: Hip orientation

R1 is the dihedral angle between the deck and the bottom face of the hip/valley rafter.

### cos2 DD

### cos2 DD

##### tan R5B = (cos2 DD tanR1) / cos DD = tanR1 cos DD

tan R5P = tanR1 / (1 / sin DD) = tanR1 sin DD

Same R5 angle formulas as the previous analysis.

Also: P6 = (90 – R5P) – (90 – SS) = SS – R5P

### Valley orientation:

The deck is a level plane, with the plane of the bottom shoulder of the valley dropping away from the deck.

R4B

Q2

## Dihedral angle between side face and bottom face of Valley rafter = 90 degrees.

Dihedral angle between Roof plane and bottom face of Valley rafter = C5.

DD

Angles to expect at intercept of Valley Peak meets Ridge or Header:

DD, R4B, R5B, A5B

MAIN SIDE VIEW

For the sake of clarity, only some of the major angles on the model faces have been labeled. Exploded views will show the remaining angles in more detail.

The planes that form the boundaries of the model (planes of R4 and R5 angles) are the same planes created by cutting a plane on the top of a post to conform to the bottom face of a Hip/Valley rafter. Expect R1, A5, R4, and R5 angles at Valley meets Post.

Working point for purlin related angles.

Anticipated angles where Valley Foot meets Main Common Rafter or Eave:

90 – DD, R4P, R5P, A5P, P6

R5B

R1

P1

###### C5

SS

90-R1

Dihedral angle =

90-A5P

90-P6

Mutually perpendicular lines

90-R5P

R4P

SS

###### C5

P1

Q2

DD

R1

R5B

R4B

NOTES:

Three mutually perpendicular lines form one of the vertices (see “Purlin kernel extracted from Hip kernel”); the kernels may positioned with any face containing a right angle as the “deck”. The angle arrangements shown above match those of the kernels extracted from the stick.

The kernels may be split along their respective dihedral angles: Valley peak meets Main Purlin along 90-C2, 90-C1 or P2, and Valley foot meets Main Common along 90-A5P, 90-DD or 90-P2. Each split produces an arrangement of angles as per a standard Hip kernel. The alternate exploded view depicts the kernels split along dihedral angles P2 and 90-P2.

Angles that upon casual inspection seem to have no direct connection to one another are now related through their respective kernels, which may be used for dimensioning as well as simply producing formulas. In addition, since the groups of angles are now defined, and a given angle occurs in more than one kernel, angular values may be determined empirically by developing the kernels using compass and straightedge only.

The sample equations given on the following page cover only a very few possible formulas.

Dihedral angle = 90-P2

Dihedral angle = 90-DD

Valley peak meets Main Purlin  (opposite hand)

1

Valley foot meets Main Common Rafter

SS

###### C5

P1

Q2

DD

R1

R5B

R4B

SS

90-R2

P1

Q2

C5

C5

90-P3

90-R3

* Dihedral angle = P2

* Dihedral angle =

90-P2

Dihedral angle =

90-DD

Dihedral angle =

90-C2

Dihedral angle =

90-C1

Valley peak meets Main Purlin

Valley foot meets Main Common Rafter

* Note: See alternate diagram of kernels extracted from model.

Dihedral angle = 90-A5P

Dihedral angle = 90-C2

Dihedral angle = 90-C1

90-R5P

Q2

Dihedral angle = P2

1

90-R3

90-R2

C5

C5

90-R1

R4P

Dihedral angle = 90-C2

Dihedral angle = 90-DD

Dihedral angle = 90-C1

Dihedral angle = 90-A5P

R4P

C5

C5

C5

C5

##### P2

P2

90-P2

P3

90-P2

90-R3

P6

90-R2

90-R1

90-P1

Note that the two kernels above may be combined along the plane of C5 to create a new kernel.

The two kernels may be combined along the plane of C5 to create the kernel examined in  “Extracting the Purlin kernel from the Hip kernel”.

90-SS

DD

90-C2

Valley Peak

Main Common Rafter

Main Purlin

D

90-DD

90-R3

90-R2

Dihedral Angle = 90-C1

90-R3

##### Q2

90-R2

For the purpose of clarity, backing angles and other cuts are not shown.

Valley Foot meets Adjacent Common Rafter: same kernel as Valley Foot meets Main Common Rafter, substitute adjacent side values.

Also anticipate these angular values at Valley meets Post or Eaves.

90-R5P

90-R1

R4P

90-A5P

Valley Peak

Dihedral Angle = 90-DD

R4P

90-R1

Valley Foot

Valley Peak meets Main Purlin

DD projected to bottom shoulder of Valley is 90-R3

Valley Foot meets Main Common Rafter

90-DD projected to bottom face of Valley is R4Pm

(90-D projected is R4Pa at Adjacent Common Rafter)

Valley Peak meets Header

DD projected to bottom plane of Valley is R4Bm

Dihedral Angle = DD

Valley Peak

90-R1

##### 90-R5Bm

R4Bm

90-R1

Valley Peak

Dihedral Angle = D

Plan

The same angles  occur at Valley meets Post.

90-R1

R4Ba

90-A5Ba

90-R5Ba

DD

D

R4Bm

Valley Peak meets Valley Peak

D projected to bottom face of Valley is R4Ba

R4Ba

90-R1

Header

90-A5Bm

Valley Peak

Plan

Note the lines that represent Common Rafter or Purlin Depth : Valley Depth. The ratio cosC5 = cosSS / cosR1 = cosP1 / cosR2 plays a role in determining the location of angle C5.

##### Dihedral angle = 90 – A5B

### 1

##### R4P

# R5P

# DD

# DD

# 90 - DD

##### R4Bm

##### R4Pa

##### R4Pm

#### R4Ba

##### SS

##### R5Pm

##### R1

##### R5Bm

##### R1

##### R4B

##### R1

##### Dihedral angle = 90 – A5P

### 1

##### R5B

### Kernels re-scaled to “Hip run” = 1: Compare the drawings below to the models extracted directly from the Valley rafter in the previous section, as well as the kernels extracted from the stick.