# Text boxes

## Rectangular Section equivalent to a Circular Section

3

D 2

4

# Setting the values of I equal, and d = D, ensures both beams have equal resisting moments and deflections.*

c, the distance from the neutral axis to the extreme fibre, is also equal for both sections.

These conditions are satisfied if

Comparing the two areas, the rectangle area is only 3/4 of the area of the circle. The maximum shear stress of the circular section is 2/3 that of the rectangular section.

D = d

b

D 4

64

Circle: A =

Rectangle: I =

Rectangle: A = bd

Circle: I =

bd 3

12

# Setting the values of I equal,

# and the rectangle depth d = D:

# Substituting equivalent Circle values,

# Rectangle A =

D 4

64

bd 3

12

=

, and b =

3D

16

3D 2

16



32M

 F b

D =

5wl 4

384 EI

F b

I

c

* For a uniformly loaded beam, supported at the ends:

M r =        , and deflection  =