Development of SS, DD, R1, and P2 Angles

## Development of C5 Angles

## Development of R4B Angles

Development of R4P Angles

# Text boxes

# Development of Hip Kernel

Main Side

SS

DD

R1

P2

# Plan showing Deck angles DD and D, and Hip pitch angle R1. Rises of the Common pitch angles SS, S, and R1 are all equal (the line segment labelled tan R1).

Deck angles DD and D are located at the Hip eaves or Valley ridges. Angles resulting from a projection of the Deck angles will follow this pattern.

W = DD + D, where

0 < W < 180 degrees

R1

D

DD

1

The trig lengths given for the line segments on the drawings may be disregarded, and the developments drawn using only a straightedge and a compass to scale the line segments marked equal.

tan R1

Plumb backing angle A7 may be developed by sustituting the Hip rise tan R1 for line segment sin R1

tan A7m = tan R1 ÷ tan DD

tan A7a = tan R1 ÷ tan D

# tan D

# C5a

# tan R1

# sin R1

# tan DD

R1

1

# C5m

D

DD

Produce the lines defining the Hip eaves or Valley ridges

W = DD + D, where 0 < W < 180 degrees

Construct the triangle of Hip Pitch angle R1

Construct line segment sin R1

Rotate line segment sin R1 to the line of the Hip run produced

Construct line segments tan DD and tan D

perpendicular to the Hip run

Draw the line segments (hypotenuse) for C5 angles

tan C5m = sin R1 ÷ tan DD

tan C5a = sin R1 ÷ tan D

If W is not equal to 90 degrees, a second development is required, beginning at angles

90 – DD and 90 – D, diagonally opposite the deck angles in the diagram. Repeat the process outlined below to solve the R4P angles, located at the Hip peak or Valley foot.

# tan D

R4Ba

1 ÷ cos R1

1

R1

# tan DD

DD

D

R4Bm

Produce the lines defining the Hip eaves or Valley ridges

W = DD + D, where 0 < W < 180 degrees

Construct the triangle of Hip Pitch angle R1

Rotate the hypotenuse 1 ÷ cos R1 to the Hip run

Construct the line segments tan DD and tan D perpendicular to the Hip run

Construct the parallel sets of line segments tan DD and tan D

perpendicular to the Hip run produced to 1 ÷ cos R1

Draw the line segments (hypotenuse) for R4B angles

tan R4Bm = tan DD ÷ (1 ÷ cos R1) = tan DD cos R1

tan R4Ba = tan D ÷ (1 ÷ cos R1) = tan D cos R1

The R4B angles are projections of the Deck angles, and are

located at the Hip eaves or Valley ridges. For W = 90 degrees, the angles

developed above are sufficient, as the values may be transferred from Main

ridge to Adjacent eave, and Adjacent ridge to Main eave.

90 – D

90 – DD

1

R4Pm

R4Pa

R1

tan (90 – D)

= 1÷ tan D

1÷ cos R1

Only one development is required for W = 90 degrees.

Angles may be transferred from Main ridge to Adjacent eave, and Adjacent ridge to Main eave.

tan (90 – DD)

= 1÷ tan DD

Produce the lines in plan representing 180 – W = 90 – DD + 90 – D

Construct the triangle of Hip Pitch angle R1

Rotate hypotenuse 1 ÷ cos R1 to the Hip run

Construct the line segments tan (90 – DD) and tan (90 – D)

perpendicular to the Hip run

Construct the parallel sets of line segments tan (90 – DD) and

tan (90 – D) perpendicular to the Hip run produced to 1 ÷ cos R1

Draw the line segments (hypotenuse) for R4B angles

tan R4Pm = (1 ÷ tan DD) ÷ (1 ÷ cos R1) = cos R1 ÷ tan DD

tan R4Pa = (1 ÷ tan D) ÷ (1 ÷ cos R1) = cos R1 ÷ tan D

The R4P angles are projections of the complements of the Deck

angles, and are located at the Hip peak or Valley foot.

1 ÷ cos R1

cos DD

sin DD

1

sin DD

cos SS

tan R1

R1